## Slide 1: Memory

## Slide 2: Outline
Memory Write Ability and Storage Permanence
Common Memory Types
Composing Memory
Memory Hierarchy and Cache
Advanced RAM

## Slide 3: Introduction
Embedded system’s functionality aspects
  Processing
    processors
    transformation of data
  Storage
    memory
    retention of data
  Communication
    buses
    transfer of data

## Slide 4: Memory: basic concepts
Stores large number of bits
  m x n: m words of n bits each
  k = Log2(m) address input signals
  or m = 2^k words
  e.g., 4,096 x 8 memory:
    32,768 bits
    12 address input signals
    8 input/output data signals
Memory access
  r/w: selects read or write
  enable: read or write only when asserted
  multiport: multiple accesses to different locations simultaneously
m × n memory
…
…
n bits per word
m words
enable
2k × n read and write memory
A0
…
r/w
…
Q0
Qn-1
Ak-1
memory external view

## Slide 5: Write ability/ storage permanence
Traditional ROM/RAM distinctions
  ROM
    read only, bits stored without power
  RAM
    read and write, lose stored bits without power
Traditional distinctions blurred
  Advanced ROMs can be written to
    e.g., EEPROM
  Advanced RAMs can hold bits without power
    e.g., NVRAM
Write ability
  Manner and speed a memory can be written
Storage permanence
  ability of memory to hold stored bits after they are written
Write ability and storage permanence of memories,
showing relative degrees along each axis (not to scale).
External
programmer
OR in-system,
block-oriented
writes, 1,000s
of cycles
Battery
life (10
years)
Write
ability
EPROM
Mask-programmed ROM
EEPROM
FLASH
NVRAM
SRAM/DRAM
Storage
permanence
Nonvolatile
In-system
programmable
Ideal memory
OTP ROM
During
fabrication
only
External
programmer,
1,000s
of cycles
External
programmer,
one time only
External
programmer
OR in-system,
1,000s
of cycles
In-system, fast
writes,
unlimited
cycles
Near
zero
Tens of
years
Life of
product

## Slide 6: Write ability
Ranges of write ability
  High end
    processor writes to memory simply and quickly
    e.g., RAM
  Middle range
    processor writes to memory, but slower
    e.g., FLASH, EEPROM
  Lower range
    special equipment, “programmer”, must be used to write to memory
    e.g., EPROM, OTP ROM
  Low end
    bits stored only during fabrication
    e.g., Mask-programmed ROM
In-system programmable memory
  Can be written to by a processor in the embedded system using the memory
  Memories in high end and middle range of write ability

## Slide 7: Storage permanence
Range of storage permanence
  High end
    essentially never loses bits
    e.g., mask-programmed ROM
  Middle range
    holds bits days, months, or years after memory’s power source turned off
    e.g., NVRAM
  Lower range
    holds bits as long as power supplied to memory
    e.g., SRAM
  Low end
    begins to lose bits almost immediately after written
    e.g., DRAM
Nonvolatile memory
  Holds bits after power is no longer supplied
  High end and middle range of storage permanence

## Slide 8: ROM: “Read-Only” Memory
Nonvolatile memory
Can be read from but not written to, by a processor in an embedded system
Traditionally written to, “programmed”, before inserting to embedded system
Uses
  Store software program for general-purpose processor
    program instructions can be one or more ROM words
  Store constant data needed by system
  Implement combinational circuit
2k × n ROM
…
Q0
Qn-1
A0
…
enable
Ak-1
External view

## Slide 9: Example: 8 x 4 ROM
Horizontal lines = words
Vertical lines = data
Lines connected only at circles
Decoder sets word 2’s line to 1 if address input is 010
Data lines Q3 and Q1 are set to 1 because there is a “programmed” connection with word 2’s line
Word 2 is not connected with data lines Q2 and Q0
Output is 1010
8 × 4 ROM
3×8 decoder
Q0
Q3
A0
enable
A2
word 0
word 1
A1
Q2
Q1
programmable connection
wired-OR
word line
data line
word 2
Internal view

## Slide 10: Implementing combinational function
Any combinational circuit of n functions of same k variables can be done with 2^k x n ROM
Truth table
Inputs (address) Outputs
a b c y z
0 0 0 0 0
0 0 1 0 1
0 1 0 0 1
0 1 1 1 0
1 0 0 1 0
1 0 1 1 1
1 1 0 1 1
1 1 1 1 1
0 0
0 1
0 1
1 0
1 0
1 1
1 1
1 1
z
y
c
enable
a
b
8×2 ROM
word 0
word 1
word 7

## Slide 11: Mask-programmed ROM
Connections “programmed” at fabrication
  set of masks
Lowest write ability
  only once
Highest storage permanence
  bits never change unless damaged
Typically used for final design of high-volume systems
  spread out NRE cost for a low unit cost

## Slide 12: OTP ROM: One-time programmable ROM
Connections “programmed” after manufacture by user
  user provides file of desired contents of ROM
  file input to machine called ROM programmer
  each programmable connection is a fuse
  ROM programmer blows fuses where connections should not exist
Very low write ability
  typically written only once and requires ROM programmer device
Very high storage permanence
  bits don’t change unless reconnected to programmer and more fuses blown
Commonly used in final products
  cheaper, harder to inadvertently modify

## Slide 13: EPROM: Erasable programmable ROM
.
(d)
(a)
(b)
source
drain
+15V
source
drain
0V
(c)
source
drain
floating gate
5-30 min
Programmable component is a MOS transistor
  Transistor has “floating” gate surrounded by an insulator
  (a) Negative charges form a channel between source and drain storing a logic 1
  (b) Large positive voltage at gate causes negative charges to move out of channel and get trapped in floating gate storing a logic 0
  (c) (Erase) Shining UV rays on surface of floating-gate causes negative charges to return to channel from floating gate restoring the logic 1
  (d) An EPROM package showing quartz window through which UV light can pass
Better write ability
  can be erased and reprogrammed thousands of times
Reduced storage permanence
  program lasts about 10 years but is susceptible to radiation and electric noise
Typically used during design development

## Slide 14: EEPROM: Electrically erasable programmable ROM
Programmed and erased electronically
  typically by using higher than normal voltage
  can program and erase individual words
Better write ability
  can be in-system programmable with built-in circuit to provide higher than normal voltage
    built-in memory controller commonly used to hide details from memory user
  writes very slow due to erasing and programming
    “busy” pin indicates to processor EEPROM still writing
  can be erased and programmed tens of thousands of times
Similar storage permanence to EPROM (about 10 years)
Far more convenient than EPROMs, but more expensive

## Slide 15: Flash Memory
Extension of EEPROM
  Same floating gate principle
  Same write ability and storage permanence
Fast erase
  Large blocks of memory erased at once, rather than one word at a time
  Blocks typically several thousand bytes large
Writes to single words may be slower
  Entire block must be read, word updated, then entire block written back
Used with embedded systems storing large data items in nonvolatile memory
  e.g., digital cameras, TV set-top boxes, cell phones

## Slide 16: RAM: “Random-access” memory
Typically volatile memory
  bits are not held without power supply
Read and written to easily by embedded system during execution
Internal structure more complex than ROM
  a word consists of several memory cells, each storing 1 bit
  each input and output data line connects to each cell in its column
  rd/wr connected to every cell
  when row is enabled by decoder, each cell has logic that stores input data bit when rd/wr indicates write or outputs stored bit when rd/wr indicates read
enable
2k × n read and write memory
A0
…
r/w
…
Q0
Qn-1
Ak-1
external view
4×4 RAM
2×4 decoder
Q0
Q3
A0
enable
A1
Q2
Q1
Memory cell
I0
I3
I2
I1
rd/wr
To every cell
internal view

## Slide 17: Basic types of RAM
SRAM: Static RAM
  Memory cell uses flip-flop to store bit
  Requires 6 transistors
  Holds data as long as power supplied
DRAM: Dynamic RAM
  Memory cell uses MOS transistor and capacitor to store bit
  More compact than SRAM
  “Refresh” required due to capacitor leak
    word’s cells refreshed when read
  Typical refresh rate 15.625 microsec.
  Slower to access than SRAM
memory cell internals
Data
W
Data'
SRAM
Data
W
DRAM

## Slide 18: Ram variations
PSRAM: Pseudo-static RAM
  DRAM with built-in memory refresh controller
  Popular low-cost high-density alternative to SRAM
NVRAM: Nonvolatile RAM
  Holds data after external power removed
  Battery-backed RAM
    SRAM with own permanently connected battery
    writes as fast as reads
    no limit on number of writes unlike nonvolatile ROM-based memory
  SRAM with EEPROM or flash
    stores complete RAM contents on EEPROM or flash before power turned off

## Slide 19: Example: HM6264 & 27C256 RAM/ROM devices
Low-cost low-capacity memory devices
Commonly used in 8-bit microcontroller-based embedded systems
First two numeric digits indicate device type
  RAM: 62
  ROM: 27
Subsequent digits indicate capacity in kilobits
Device Access Time (ns) Standby Pwr. (mW) Active Pwr. (mW) Vcc Voltage (V)
HM6264 85-100 .01 15 5
27C256 90 .5 100 5
22
20
data<7…0>
addr<15...0>
/OE
/WE
/CS1
CS2
HM6264
11-13, 15-19
2,23,21,24,
25, 3-10
22
27
20
26
data<7…0>
addr<15...0>
/OE
/CS
27C256
11-13, 15-19
27,26,2,23,21,
24,25, 3-10
block diagrams
device characteristics
timing diagrams
data
addr
OE
/CS1
CS2
Read operation
data
addr
WE
/CS1
CS2
Write operation

## Slide 20: Example: TC55V2325FF-100 memory device
2-megabit synchronous pipelined burst SRAM memory device
Designed to be interfaced with 32-bit processors
Capable of fast sequential reads and writes as well as single byte I/O
timing diagram
block diagram
device characteristics
data<31…0>
addr<15…0>
addr<10...0>
/CS1
/CS2
CS3
/WE
/OE
MODE
/ADSP
/ADSC
/ADV
CLK
TC55V2325FF-100
Device Access Time (ns) Standby Pwr. (mW) Active Pwr. (mW) Vcc Voltage (V)
TC55V23 10 na 1200 3.3
25FF-100
A single read operation
CLK
/ADSP
/ADSC
/ADV
addr <15…0>
/WE
/OE
/CS1 and /CS2
CS3
data<31…0>

## Slide 21: Composing memory
Memory size needed often differs from size of readily available memories
When available memory is larger, simply ignore unneeded high-order address bits and higher data lines
When available memory is smaller, compose several smaller memories into one larger memory
  Connect side-by-side to increase width of words
  Connect top to bottom to increase number of words
    added high-order address line selects smaller memory containing desired word using a decoder
  Combine techniques to increase number and width of words
…
2m × 3n ROM
2m × n ROM
A0
…
enable
2m × n ROM
…
2m × n ROM
…
Q3n-1
Q2n-1
…
Q0
…
Am
Increase width of words
2m+1 × n ROM
2m × n ROM
A0
…
enable
…
2m × n ROM
Am-1
Am
1 × 2 decoder
…
…
…
Qn-1
Q0
…
Increase number of words
A
enable
outputs
Increase number and width of words

## Slide 22: Memory hierarchy
Want inexpensive, fast memory
Main memory
  Large, inexpensive, slow memory stores entire program and data
Cache
  Small, expensive, fast memory stores copy of likely accessed parts of larger memory
  Can be multiple levels of cache
Processor
Cache
Main memory
Disk
Tape
Registers

## Slide 23: Cache
Usually designed with SRAM
  faster but more expensive than DRAM
Usually on same chip as processor
  space limited, so much smaller than off-chip main memory
  faster access ( 1 cycle vs. several cycles for main memory)
Cache operation:
  Request for main memory access (read or write)
  First, check cache for copy
    cache hit
      copy is in cache, quick access
    cache miss
      copy not in cache, read address and possibly its neighbors into cache
Several cache design choices
  cache mapping, replacement policies, and write techniques

## Slide 24: Cache mapping
Far fewer number of available cache addresses
Are address’ contents in cache?
Cache mapping used to assign main memory address to cache address and determine hit or miss
Three basic techniques:
  Direct mapping
  Fully associative mapping
  Set-associative mapping
Caches partitioned into indivisible blocks or lines of adjacent memory addresses
  usually 4 or 8 addresses per line

## Slide 25: Direct mapping
Main memory address divided into 2 fields
  Index
    cache address
    number of bits determined by cache size
  Tag
    compared with tag stored in cache at address indicated by index
    if tags match, check valid bit
Valid bit
  indicates whether data in slot has been loaded from memory
Offset
  used to find particular word in cache line
Data
Valid
Tag
Index
Offset
=
V T D

## Slide 26: Fully associative mapping
Complete main memory address stored in each cache address
All addresses stored in cache simultaneously compared with desired address
Valid bit and offset same as direct mapping
Tag
Offset
=
V T D
Valid
V T D
…
V T D
=
=
Data

## Slide 27: Set-associative mapping
Compromise between direct mapping and fully associative mapping
Index same as in direct mapping
But, each cache address contains content and tags of 2 or more memory address locations
Tags of that set simultaneously compared as in fully associative mapping
Cache with set size N called N-way set-associative
  2-way, 4-way, 8-way are common
Tag
Index
Offset
=
V T D
Data
Valid
V T D
=

## Slide 28: Cache-replacement policy
Technique for choosing which block to replace
  when fully associative cache is full
  when set-associative cache’s line is full
Direct mapped cache has no choice
Random
  replace block chosen at random
LRU: least-recently used
  replace block not accessed for longest time
FIFO: first-in-first-out
  push block onto queue when accessed
  choose block to replace by popping queue

## Slide 29: Cache write techniques
When written, data cache must update main memory
Write-through
  write to main memory whenever cache is written to
  easiest to implement
  processor must wait for slower main memory write
  potential for unnecessary writes
Write-back
  main memory only written when “dirty” block replaced
  extra dirty bit for each block set when cache block written to
  reduces number of slow main memory writes

## Slide 30: Cache impact on system performance
Most important parameters in terms of performance:
  Total size of cache
    total number of data bytes cache can hold
    tag, valid and other house keeping bits not included in total
  Degree of associativity
  Data block size
Larger caches achieve lower miss rates but higher access cost
  e.g.,
    2 Kbyte cache: miss rate = 15%, hit cost = 2 cycles, miss cost = 20 cycles
      avg. cost of memory access = (0.85 * 2) + (0.15 * 20) = 4.7 cycles
    4 Kbyte cache: miss rate = 6.5%, hit cost = 3 cycles, miss cost will not change
      avg. cost of memory access = (0.935 * 3) + (0.065 * 20) = 4.105 cycles (improvement)
    8 Kbyte cache: miss rate = 5.565%, hit cost = 4 cycles, miss cost will not change
      avg. cost of memory access = (0.94435 * 4) + (0.05565 * 20) = 4.8904 cycles (worse)

## Slide 31: Cache performance trade-offs
Improving cache hit rate without increasing size
  Increase line size
  Change set-associativity
0
0.02
0.04
0.06
0.08
0.1
0.12
0.14
0.16
1 Kb
2 Kb
4 Kb
8 Kb
16 Kb
32 Kb
64 Kb
128 Kb
1 way
2 way
4 way
8 way
% cache miss
cache size

## Slide 32: Advanced RAM
DRAMs commonly used as main memory in processor based embedded systems
  high capacity, low cost
Many variations of DRAMs proposed
  need to keep pace with processor speeds
  FPM DRAM: fast page mode DRAM
  EDO DRAM: extended data out DRAM
  SDRAM/ESDRAM: synchronous and enhanced synchronous DRAM
  RDRAM: rambus DRAM

## Slide 33: Basic DRAM
Address bus multiplexed between row and column components
Row and column addresses are latched in, sequentially, by strobing ras and cas signals, respectively
Refresh circuitry can be external or internal to DRAM device
  strobes consecutive memory address periodically causing memory content to be refreshed
  Refresh circuitry disabled during read or write operation
Data
In Buffer
Data
Out Buffer
rd/
wr
data
Row
Addr.
Buffer
Col
Addr
. Buffer
address
ras
cas
Bit storage array
Row Decoder
Col Decoder
Refresh
Circuit
cas,
ras, clock
Sense
Amplifiers

## Slide 34: Fast Page Mode DRAM (FPM DRAM)
Each row of memory bit array is viewed as a page
Page contains multiple words
Individual words addressed by column address
Timing diagram:
  row (page) address sent
  3 words read consecutively by sending column address for each
Extra cycle eliminated on each read/write of words from same page
row
col
data
col
col
data
data
ras
cas
address
data

## Slide 35: Extended data out DRAM (EDO DRAM)
Improvement of FPM DRAM
Extra latch before output buffer
  allows strobing of cas before data read operation completed
Reduces read/write latency by additional cycle
row
col
col
col
data
data
data
Speedup through overlap
ras
cas
address
data

## Slide 36: (S)ynchronous and Enhanced Synchronous (ES) DRAM
SDRAM latches data on active edge of clock
Eliminates time to detect ras/cas and rd/wr signals
A counter is initialized to column address then incremented on active edge of clock to access consecutive memory locations
ESDRAM improves SDRAM
  added buffers enable overlapping of column addressing
  faster clocking and lower read/write latency possible
clock
ras
cas
address
data
row
col
data
data
data

## Slide 37: Rambus DRAM (RDRAM)
More of a bus interface architecture than DRAM architecture
Data is latched on both rising and falling edge of clock
Broken into 4 banks each with own row decoder
  can have 4 pages open at a time
Capable of very high throughput

## Slide 38: DRAM integration problem
SRAM easily integrated on same chip as processor
DRAM more difficult
  Different chip making process between DRAM and conventional logic
  Goal of conventional logic (IC) designers:
    minimize parasitic capacitance to reduce signal propagation delays and power consumption
  Goal of DRAM designers:
    create capacitor cells to retain stored information
  Integration processes beginning to appear

## Slide 39: Memory Management Unit (MMU)
Duties of MMU
  Handles DRAM refresh, bus interface and arbitration
  Takes care of memory sharing among multiple processors
  Translates logic memory addresses from processor to physical memory addresses of DRAM
Modern CPUs often come with MMU built-in
Single-purpose processors can be used